## Slide 1
ELECTRONICS
WORKSHOP 2
Sannidhya Gupta 2021112012
Vinkesh Bansal 2021102020
SPRING 2023
UG 2
Heart monitoring circuit (ECG, Heart rate)
Team 16
https://iiitaphyd-my.sharepoint.com/:f:/g/personal/sannidhya_gupta_research_iiit_ac_in/EgJ9QPLAHIZBlJ_w_0Rzy9MBTH6wiUdICGOZ3w0bH5IflA?e=EknYz6
Link to one drive folder:

## Slide 2
Motivation
  Understanding heart health: By displaying the heart rate, individuals can gain insights into their heart health and take necessary measures to improve it.
  Educational purposes: This project can be a great learning tool for electronics enthusiasts who want to understand how to work with ECG signals.
  Innovation: With the increasing demand for wearable technology, this project can be seen as a way to track heart rate and can be potentially added to the current range of wearable devices if refined with such motive.

## Slide 3
Literature Survey
We used the given paper to get a basic idea of how extraction of ECG works.
This paper discusses extraction and procsessing of ECG signal from the body by using 3 gel electrodes, and giving a LED output if the user's heartbeat lies outside the normal range
Link:
https://isn.ucsd.edu/courses/beng186b/project/2021/Amin_Khairil_Satish_Shah_Zaferi_Heart_rate_monitor_via_ecg.pdf

## Slide 4
Introduction
  Measuring ECG signal from the body
  Processing the signal in order to make it informative
  Analysing the signal frequency (heart rate)
  Displaying the heart rate to the user

## Slide 5
Execution blocks
  ECG signal is extracted by gel electrodes
  Amplfication
  System to remove noise
  Filters to remove unwanted bioelectronic signals
  Clock
  Display (Number of beats)
These are the subparts that we used for our circuit

## Slide 6
Extraction of signal using gel electrodes
Block Diagram
Instrumentation amplifier
Filter (Low pass and High pass)
Narrow band Notch Filter
(50 Hz)
Clock
(555 timer)
Analog to digital conversion
(555 timer)
Counter (using 4029 IC)
Display
(Using LEDs as binary bits)

## Slide 7
Instrumentation Amplifier
An instrumentation amplifier is an electronic device that is used to amplify small signals. It is a type of differential amplifier. The instrumentation amplifier is typically used in applications where the signal of interest is small and buried in a large amount of noise or other unwanted signals, such as in biomedical instrumentation

## Slide 8
Gain analysis
Theoretical Gain =1,372.96

## Slide 9
Filters - Low and High Pass
Low pass = 39.79Hz
High pass = 0.5Hz
As EMG and other signals lie outside this range
RC filters are used for this

## Slide 10
Notch Filter
A narrow band reject filter in order to reject the 50Hz noise present in the circuit

## Slide 11
Final Simulation

## Slide 12
Displaying the hearbeat
Clock
(555 timer)
Analog to digital conversion
(555 timer)
Counter (using 4029 IC)
Display
(Using LEDs as binary bits)
  ECG signal, obtained in pulses is first converted to square pulses, thus converting the hearbeat into digital domain
  A clock of time period ~ 25 seconds is constructed
  The digital signal is fed into counters after ANDing with the clock. Thus, the counter only counts when clock is on

## Slide 13
Important points
MIN MAX HEARTBEART MEASURABLE
0.7Hz to 5Hz
42bpm to 300bpm
INPUT
RANGE
The ECG has amplitude < 5mVpp, so circuit has been designed for 2mVpp
OUTPUT
RANGE
The square wave obtained as outputs have amplitude = Vcc

## Slide 14
Hardware
The potentiometer adjusts our A/D converter by adjusting the required voltage for input signal
The 8 red LED's count the heart beats and display it in binary
The green LED is the clock, it generates a high signal for T~25sec. The counter only counts when the clock signal is high

## Slide 15
CD4029 IC:
4 bit binary counter
x 2
555 timer (clock generator)
T = 25 sec
input pulses (ECG signal from heart), rectified to be in the form of digital pulses
Counting system
8 bit binary counter
AND
GATE
Asynchronous reset
(slide switch)
resets counter to zero

## Slide 16
Amplifier
Observed Gain:
1278.36
Theoretical Gain =1,372.96

## Slide 17
Frequency Response analysis of filters

## Slide 18
Analog to digital conversion
Sinusoid wave from waveform
ECG signal from human body

## Slide 20
Challenges faced
FORM OF DISPLAY USED TO OUTPUT THE HEARTBEAT
ANALYSING THE ECG AND EXTRACTING HEART RATE WITHOUT USING MICROCONTROLLER
NOISE REDUCTION - REJECTING THE PREVELANT 50HZ NOISE
ANALOG TO DIGITAL CONVERSION, AND FIGURING OUT PULSE WIDTH OF PULSE

## Slide 21
Improvements
ADDING A DIGITAL DISPLAY INSTEAD OF USING LED OUTPUTS AS BINARY BITS
MAKING THE CIRCUIT MORE ROBUST TO PROCESS ECG SIGNAL OF DIFFERENT AMPLITUDES
IMPROVING THE ECG EXTRACTION PROCESS AND USING A WAY BETTER THAN GEL ELECTRODES

## Slide 22
Thank you
  BETTER UNDERSTANDING AND WORKING WITH BIOPOTENTIAL SIGNALS
  HOW EVERY PART OF AN ELECTRONIC CIRCUIT CONTRIBUTES TO THE WHOLE PROBLEM STATEMENT
  IMPROVE OUR THINKING CAPABILITIES BY FINDING SOLUTIONS TO NEWLY ENCOUNTERED PROBLEMS AND ISSUES
Conclusion
WORKING ON THIS PROJECT HELPED US TO: